## Slide 1: Module 2
Configuring IDS and IPS

## Slide 2: Configuring IDS
Step 1. Initialization configuration Step 2. Logging or PostOffice configuration Step 3. Audit rule configuration and activation

## Slide 3: Configuring IDS
Step 1: Initialization Configuration
  Router(config)# ip audit po max-events #_of_events
  Router(config)# ip audit smtp spam #_of_recipients

## Slide 4: Configuring IDS
Step 1: Initialization Configuration
  The ip audit po max-events command limits the number of IDS events that the Cisco IOS queues up to send to a remote device.
  By default, this is 250 events, but this can range from 1 to 65,535.
  This limit is used to ensure that if a hacker tried to flood a router with a lot of attacks, the router would not overload itself in trying to process all of them.
  Otherwise, this basically would allow the hacker to create a DoS attack against the router itself.

## Slide 5: Configuring IDS
Step 1: Initialization Configuration
  The ip audit smtp spam command is used to limit e-mail spamming that uses mass mailings.
  With this command, the default number of recipients allowed in an e-mail message is 250. If an e-mail message contains more than this value, the router takes the configured action
  The number of recipients can range from 1 to 65,535.

## Slide 6: Configuring IDS
Step 2: Logging and PostOffice Configuration
  The Cisco IOS can use two methods when logging IDS events:
    log the information using syslog or log the information using an IDS Director.
    Using syslog, the Cisco IOS can log information locally (the console or the internal buffer) or remotely (a syslog server).
    If you want to use the syslog method, you must configure the following IDS statement:
    Router(config)# ip audit notify log

## Slide 7: Configuring IDS
Step 2: Logging and PostOffice Configuration
  The Cisco IOS can use two methods when logging IDS events:
    1) log the information using syslog
    2) log the information using an IDS Director.
    Using syslog, the Cisco IOS can log information locally (the console or the internal buffer) or remotely (a syslog server).

## Slide 8: Configuring IDS
    If you want to use the syslog method, you must configure the following IDS statement:
    Router(config)# ip audit notify log
If you are using CiscoWorks VMS with Security Monitoring Center (MC), you can forward the router's syslog messages to Security MC, which is used to centralize the repository and reporting of alarm information.

## Slide 9: Configuring IDS
When logging informational signatures to the router's console, you also need to execute the following command:
  Router(config)# logging console info

## Slide 10: Configuring IDS
Second logging option is to log information to an IDS Director,

## Slide 11: Configuring IDS
The ip audit notify nr-director command enables the logging of IDS events to an IDS Director product.
The ip audit po local command specifies the PostOffice configuration for the router;
the ip audit po remote command specifies the configuration for the remote Director device.

## Slide 12: Configuring IDS
With PostOffice, each device needs a unique combination of a host ID and an organization ID.
The organization ID is used to group sensors. In smaller companies, normally only a single organization ID is necessary.
For enterprise companies, you might have different organization IDs for each division, allowing for easier management of your sensor products.
Within each organization, a device needs a unique host ID. This concept is similar to IP addressing, in which you have network numbers and hosts within a network. Both of these IDs range from 1 to 65,535.

## Slide 13: Configuring IDS
Step 3: Audit Rule Configuration and Activation
  When you have defined your logging method, you are ready to create your IDS auditing rules. Two sets of commands are used to configure audit rules: global (default actions) and specific.
  Global Policies
    Global policies are used to take the appropriate actions for matching on signatures, unless a specific rule designates otherwise. To create your global policies, use these two commands:
      Router(config)# ip audit info {action [alarm] [drop] [reset]}
      Router(config)# ip audit attack {action [alarm] [drop] [reset]}

## Slide 14: Configuring IDS
As you can see, the two commands specify actions for informational and attack signatures. Each has three possible actions that the router can take:
  alarm? Generate an alarm (log), where this is the default action
  drop? Drop the packet
  reset? For TCP connections, tear down the connection
These commands need to be configured only if you want to change the default action (alarm) and you want the Cisco IOS IDS engine to use the same policy for all traffic of the same signature category.

## Slide 15: Configuring IDS
Specific Policies
  Besides globally changing the behavior or IDS, you can create specific IDS auditing policies.
  Typically, you do this if you have two interfaces on your router?perhaps one connected to the Internet and the other to a remote site?and you want to set up different IDS policies (actions to signature matches) for each interface.

## Slide 16: Configuring IDS
Specific Policies
  Here is the command syntax to set up your specific IDS auditing policies:

## Slide 17
http://etutorials.org/Networking/Router+firewall+security/Part+VII+Detecting+and+Preventing+Attacks/Chapter+16.+Intrusion-Detection+System/IDS+Configuration/
https://www.ciscopress.com/articles/article.asp?p=24696&seqNum=5