## Slide 1: Module-3
Testing and Troubleshooting of Security Devices

## Slide 2: Module-3: Device Configuration
Common issues in installing or configuring information security devices
Methods to resolve these issues
Methods of testing installed/configured information security devices

## Slide 3: Common Router problems and solutions
Ping:
  Use the ping and trace commands to check for connectivity.
Check the Routing Table:
  Use the show ip route or show ipv6 route command to find out what the router knows. Is there either an explicit route to the remote network or a gateway of last resort?

## Slide 4: Common Router problems and solutions
Is there a Firewall on the Computer?
  If the problem involves a computer, check to ensure that its firewall is not blocking packets.
  Sometimes there are computers at client locations with firewalls in operation without the client’s knowledge.

## Slide 5: Common Router problems and solutions
Any Access Lists?
  If the above steps don’t resolve the issue, check for access-control lists that block traffic.
  There is an implicit “deny any” at the end of every access-control list, so even if you don’t see a statement explicitly denying traffic, it might be blocked by an implicit “deny any.”

## Slide 6: Common Router problems and solutions
Is the VPN Up?
  If a VPN is part of the connection, check to ensure that it is up. Use the show crypto family of commands to check VPN connections.
  With VPN connections, each end of the connection must mirror the other.
  For example, even something as seemingly inconsequential as a different timeout value or a different key lifetime can prevent a connection.

## Slide 7: Common Router problems and solutions
Do the Protocols Match?
  If you are trying to gain remote access to a server, ensure that it supports the protocol you’re attempting to use.
  For example, if the router hasn’t been configured to support SSH and you use the default settings in PuTTY which call for SSH, you won’t be able to connect.
  Also, some admins change the default port numbers, so you may expect to use port 22 with SSH, but the admin may have configured it to use a non-standard port.

## Slide 8: Common Router problems and solutions
Check for Human Error:
  User errors can also be the source of errors. Check to ensure that correct usernames and passwords are being used, that you and the admin on the other end of the connection are using the same network addresses and matching subnet masks.
Verify Settings:
  Do not make assumptions. Verify everything!

## Slide 9: Router Troubleshooting Tools
Using Router Diagnostic Commands
  Cisco routers provide numerous integrated commands to assist you in monitoring and troubleshooting your internetwork.

## Slide 10: Router Troubleshooting Tools
Using show Commands
  The show commands are powerful monitoring and troubleshooting tools.
    Monitor router behaviour during initial installation
    Monitor normal network operation
    Isolate problem interfaces, nodes, media, or applications
    Determine when a network is congested
    Determine the status of servers, clients, or other neighbours

## Slide 11: Router Troubleshooting Tools
Using debug Commands
  The debug privileged exec commands can provide a wealth of information about the traffic being seen (or not seen) on an interface, error messages generated by nodes on the network, protocol-specific diagnostic packets, and other useful troubleshooting data.
  In many situations, using third-party diagnostic tools can be more useful and less intrusive than using debug commands.

## Slide 12: Router Troubleshooting Tools
Using the ping Command
  To check host reachability and network connectivity, use the ping exec (user) or privileged exec command.
  After you log in to the router or access server, you are automatically in user exec command mode. The exec commands available at the user level are a subset of those available at the privileged level.
  In general, the user exec commands allow you to connect to remote devices, change terminal settings on a temporary basis, perform basic tests, and list system information.
  The ping command can be used to confirm basic network connectivity on AppleTalk, ISO Connectionless Network Service (CLNS), IP, Novell, Apollo, VINES, DECnet, or XNS networks.

## Slide 13: Router Troubleshooting Tools
Using the trace Command
  The trace user exec command discovers the routes that a router’s packets follow when traveling to their destinations.
  The trace privileged exec command permits the supported IP header options to be specified, allowing the router to perform a more extensive range of test options.